## Slide 1: Parallel TCP
Weice Sun, Zhongyi Luo, Siyuan Peng, Mengying Du, Qiang Wang

## Slide 2: What is Parallel TCP?
Data set is divided into a number of smaller chunks, and each component chunk is transmitted using its own TCP session.

## Slide 3: Project Objective
Parallel TCP Real Implementation
NS 3 Simulation
Data Analysis

## Slide 4: Parallel TCP Real Implementation
Design Principles
Coding Methods
Testing
Data Analysis

## Slide 5: Program Flowchart
-- Sender
Start
Check IP
Get destination IP and file path
Check file path
Get Respond
Yes
No
No
Divide the file into n chunks
Read file into corresponding buffer
Send handshake packet to the receiver
Establish parallel connections to send file chunks
Yes
Print Error

## Slide 6: -- Receiver
Start
Ports start listening
Reorder data from sockets
Read into a buffer
Write data to a new file
Establish connection
Send ACK to sender
end
Yes
No

## Slide 7: Test Results
Data Transferred via Parallel TCP
Exactly the same!

## Slide 8: Data Analysis
Chart: T.csv
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
 | 0.89757 | 1.1423 | 0.85922 | 0.85975 | 1.175 | 1.0886 | 1.2215 | 1.2031
Chart: Downtown menreol image
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
 | 0.041651 | 0.04204 | 0.04576 | 0.048014 | 0.048294 | 0.058484 | 0.05546 | 0.064015
Chart: Face video
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Port Number | 0.34709 | 0.29041 | 0.32315 | 0.28592 | 0.29737 | 0.31391 | 0.3373 | 0.33239
Is there a trend?
What this implies?
What we do next?

## Slide 9: Parallel TCP fairness ---ns3 simulation
Topology:
Simulation Environment:
  OSX 10.10.5 2.9 GHz Intel Core i5
  ns-3.24.1
  Global parameter setting:
    Random seed: RngSeedManager::SetSeed(11223344)
    Protocol TCP Reno
    Segment Size = 512
    BW and delay: 5Mbps 10ms & 1Mbps 20ms
Sender
Sink

## Slide 10: Parallel TCP throughput & standard deviation -- simulation result
Queuing Mode
Window Size
Queue Size
Port Number
DropTail Queue
{2000 Bytes
- 32000 Bytes}
{8000 Bytes
- 64000 Bytes}
{4 - 9}
+- 15%
Port # 4-6
Better fairness

## Slide 11: Parallel TCP throughput & standard deviation -- simulation result
Queuing Mode
Window Size
Queue Size
Port Number
RED
Queue
{2000 Bytes
- 32000 Bytes}
{8000 Bytes
- 64000 Bytes}
{4 - 9}
+- 10%
Max Thresh: 0.24 * QueueSize;
Min Thresh: 0.04 * QueueSize;
Better fairness
Port # 4-5

## Slide 12: Parallel TCP throughput & standard deviation -- simulation result
Queuing Mode
Window Size
Queue Size
Port Number
RED
Queue
{2000 Bytes
- 32000 Bytes}
{8000 Bytes
- 64000 Bytes}
{4 - 9}
+- 18%
Max Thresh: 0.1 * QueueSize;
Min Thresh: 0.04 * QueueSize;
Better fairness
Port # 4-6

## Slide 13: Parallel TCP throughput & standard deviation -- simulation result
Queuing Mode
Window Size
Queue Size
Port Number
RED
Queue
{2000 Bytes
- 32000 Bytes}
{8000 Bytes
- 64000 Bytes}
{4 - 9}
+- 22%
Max Thresh: 0.004 * QueueSize;
Min Thresh: 0.0001 * QueueSize;
Better fairness
Port # 4-6

## Slide 14: Conclusion:
Implementation
  Validity
  Robustness
  Efficiency
Simulation
  Throughput
  Fairness

## Slide 15: Q&A